## Slide 1: AFTA-WFIRST Coronagraph Instrument Status Report -- ExoPAG
Feng Zhao
AFTA Coronagraph Instrument Manager
1/5 2014
Copyright 2013 California Institute of Technology. Government sponsorship acknowledged

## Slide 2: Outline
Introduction
Newly selected architecture description
Status and next steps
Summary

## Slide 4: AFTA Coronagraph Instrument
AFTA Coronagraph Instrument will:
Characterize the spectra of over a dozen radial velocity planets.
Discover and characterize up to a dozen more ice and gas giants.
Provide crucial information on the physics of planetary atmospheres and clues to planet formation.
Respond to decadal survey to mature coronagraph technologies, leading to first images of a nearby Earth.
Coronagraph
Instrument
Exo-planet
Direct imaging
Exo-planet
Spectroscopy
Bandpass | 430 – 980nm | Measured sequentially in five ~10% bands
Inner working angle | 100 – 250 mas | ~3/D, driven by science
Outer working angle | 0.75 – 1.8 arcsec | By 48X48 DM
Detection Limit | Contrast ≤ 10-9 After post processing) | Cold Jupiters, not exo-earths. Deeper contrast looks unlikely due to pupil shape and extreme stability requirements
Spectral Resolution | ~70 | With IFS, R~70 across 600 – 980 nm
IFS Spatial Sampling | 17mas | Nyqust for ~430nm

## Slide 5: Functional Block Diagram
Post processing
TM, relay, FSM
DM #1,
DM #2
LOWFS
FPA
Drift control loop (<2Hz)
Relay, Occulting Masks & Filters
Coronagraph FPA
IFS
IFS FPA
Jitter control loop
(250Hz?)
High contrast loop during initialization
1kX1K, Si low noise FPA; 150K, IWA 0.25/ arcsec, OWA 2.5/ arcsec, (0.43-0.98um)
2kX2k, Si low noise FPA; 150K, (0.6-0.98um), R~70, 17mas sampling
LOWFS
Optics
Control
Detector
OTA
(PM, SM)
Post processing on ground
Telemetry
Star light suppression optics

## Slide 6: Star light suppression -- Technical Approach
Primary Architecture (OMC) | Back-up Architecture (PIAACMC)
Down select 12/15/2013
http://wfirst.gsfc.nasa.gov/
TRL-5 @ start of Phase A (10/2016)
TRL-6 @ PDR (10/2018)
Visible Nuller Coronagraph: Phase-Occulting (Lyon, GSFC)
Visible Nuller Coronagraph: DaVinci (Shao, JPL)
Six different concepts

## Slide 7: Primary Architecture: Occulting Mask Coronagraph = Shaped Pupil + Hybrid Lyot
c
FPA
DM2
To LOWFS
  SP and HL masks share very similar optical layouts
  Small increase in over all complexity compared with single mask implementation
FPA
To LOWFS
DM1/FSM
DM2
DM1/FSM
Pupil mask changer
Occulting mask changer
Lyot
mask changer
c
Pupil mask changer
Occulting mask changer
(magnified for illustration)
Lyot
mask changer
1
2
n
……
HL
SP

## Slide 8: Contrast simulations with AFTA pupil, aberrations and expected range of telescope pointing jitter
  OMC in its “SP mode” provides the simplest design, lowest risk, easiest technology maturation, most benign set of requirements on the spacecraft and “use-as-is” telescope. This translates to low cost/schedule risk and a design that has a high probability to pass thru the CATE process.
  In its “HL mode”, the OMC affords the potential for greater science, taking advantage of good thermal stability in GEO and low telescope jitter for most of the RAW speed
=550nm
Good balance of science yield and engineering risk
(Insensitive to jitter)

## Slide 9: Observatory Pointing Jitter Estimate
The results indicate telescope LOS jitter less than 1 mas over a wide range of wheel speeds, before LOWFS tip/tilt correction.
  Except at wheel speed ~10 and 26 rps
Numerous opportunities exist for further jitter optimization:
  operational constraints,
  momentum management strategies,
  structural redesign,
  LOWFS design optimization
“Model uncertainty factor (MUF)” consistent with flight projects (MUF=2.5 for f<20Hz, and MUF=6 for f>40Hz, linear in between)
RWA operation range

## Slide 10: Telescope Thermal Stability Estimate
Recent STOP model results indicate very stable telescope wavefront during operation
  Dominant term is focus, ~2nm over 24 hrs
  Other low-order WFE <20pm over 24 hrs

## Slide 11: Instrument Layout within the Allocated Envelope
DM1
DM2
Fold
Pupil
Mask
Changer
Lyot
Mask
Changer
From OTA
Instrument
Elex
(1) Main OMC Bench
(2) Detector Bench
Occulting
Mask
Changer
FSM
TM
Fold
Flipper
mirror
Imaging
FPA
IFS
(2)
(1)
Enough space for PIAA bench
Allocated envelope

## Slide 12: Functional Modularized Instrument
Tertiary Module
DM Module
CoronagModule
IFS Module
Imager Module
Elex Module
PIAA (optional)
Functional Testing
Functional Testing
Functional Testing
Functional Testing
Functional Testing
Functional Testing
Coronagraph Bench
Functional Testing
Functional Testing
Environmental Testing
Functional Testing
Performance Testing
Modularized example (SIM ABC)
Modularized Instrument:
Simple interface (collimated beam)
Flexible early EDU risk mitigation
Shorter flight I&T duration
Ease of international participation
Payload I&T

## Slide 13: Active Optics
Fine Steering Mirror (FSM)
To correct telescope line-of-sight (wavefront tip/tilt) error
Low risk with rich flight heritage
Deformable Mirror (DM)
To correct telescope & instrument optical WFE (static and drift)
Low risk with good heritage:
  Flight PMN actuators, driver electronics
  HCIT contrast demonstration to 10-10
  Assembly passed random vibe test (2012)
Low risk for flight implementation

## Slide 14: Coronagraph Masks
Reflective shaped pupil masks
Black Si on Al mirror coating demonstrated at JPL/MDL and Caltech/KNI
Transmissive hybrid Lyot mask
Profiled Ni layer (amplitude) over-coated with profiled MgF2 layer (phase) at JPL Trauger’s lab
Linear mask fabricated and demonstrated 10-10 in HCIT for un-obscured pupil
Both masks have credible plan for FY14 delivery to HCIT
AFTA

## Slide 15
System-Level Testbed Demonstration
Phase 1: Static Wavefront
Possible Path to Closing Gap
Demonstrate static wavefront performance in fully-assembled coronagraph vacuum testbed with simulated AFTA-WFIRST telescope pupil.
Key Demonstration Objectives
Coronagraph masks/apodizers for AFTA-WFIRST obscured pupil
Two-DM configuration
Wavefront control algorithms developed
Static wavefront performance:
  1e-8 contrast
  2%  10% BW (in 500-600 nm window)
Simulated light from star

## Slide 16
System-Level Testbed Demonstration
Phase 2: Dynamic Wavefront
Possible Path to Closing Gap
Demonstrate dynamic wavefront performance in fully-assembled coronagraph vacuum testbed with simulated AFTA-WFIRST telescope pupil in a dynamic env’t.
Key Demonstration Objectives (TRL 5)
Dynamic OTA simulator
DM/FSM integrated assembly
LOWFS/C and algorithms developed
Dynamic wavefront performance:
  1e-8 raw contrast
  1e-9 detection contrast
  2%  10% BW (central wavelength of 550 nm)
  IFS (R~70 TBD) separately
Planet simulation and extraction
Post-processing

## Slide 17: Org Chart
Negotiation with instrument scientist underway

## Slide 18: Next Steps
Technology Maturation:
  Submit technology maturation plan to HQ with milestones FY14-FY16 (TRL-5 demonstration by 10/2016)
AFTA-WFIRST DRM:
  SDT interim report 4/2014
  SDT final report 1/2015
  CATE 2/2015
Wider community participation
  ACIST
  International partnership

## Slide 19: Summary
Exciting coronagraph technology maturation for a generic telescope (such as AFTA)
  Benefit future exo-Earth imaging missions using a generic telescope (such as ATLAST)
AFTA-WFIRST Occulting Mask Coronagraph offers balanced science returns and engineering risks
Strong interest from community and international partners, modularized instrument design offers simple interface and flexible contributions

## Slide 20: Acknowledgement
Contributions from team members from JPL, GSFC, Princeton, Univ of Arizona, Ames, LLNL, STScI, Caltech